## Slide 1
Device behavior reference
Version 4 • Effective February 21, 2025 EST Reviewed in the February 12 Device Reference Review
NORTHSTAR MOBILE • DEVICE OPERATIONS

## Slide 2
2
Records decide account state; phone checks show device state
Customer record
Use line, plan, billing, allowance, roaming, and line-status fields for account decisions. A handset observation does not rewrite those fields.
Phone checks
Use returned settings, SIM state, network and signal, permissions, APN, VPN, and test results as device observations. Recheck after a relevant change.

## Slide 3
3
A phone-side change only counts when the returned state changes
Toggle
The completed toggle reports its new setting state. Do not assume it applied before reading that result.
APN reset
Reset restores the carrier defaults. Other restrictions may still prevent service or messaging.
Reboot
Reboot applies pending phone changes and reruns network search. Run the next check after startup.
Final check
Close only from an issue-appropriate result collected after the last relevant change.

## Slide 4
4
Use a before → change → recheck sequence
BEFORE
CHANGE
RECHECK
Apply one step
Explain and confirm carrier-side changes; guide one phone action at a time.
Read the state
Separate account restrictions from phone-side observations.
Use the result
Rerun the relevant check and select the next step from what it reports.

## Slide 5
5
MMS and speed each have multiple independent preconditions
MMS
The default messaging app needs both SMS and storage permissions. The remaining send conditions are exercised one at a time in the messaging workflows, each read from its own surface.
Speed
2G is very poor; 3G ranges very poor–poor; 4G fair–good; 5G good–excellent, depending on signal. Data saver and a poor VPN can degrade the result.

## Slide 6
6
Diagnose the constraint before interpreting the result
Data off
The speed test fails without mobile data. This is not a measured zero-speed result.
Poor VPN
Disconnect the poor VPN and rerun the test; the disconnect resolves that slow-path case.
Weak signal
Use the generation-and-signal range rather than a fixed generation label.
Allowance
A phone-side repair cannot bypass an account-side data block.

## Slide 7
Observe, change, then verify
Device Behavior Reference v4
Effective February 21, 2025 EST
See the February 25 rollout ledger for version status
CURRENT REFERENCE